Chip back potential is the level which bulk silicon is maintained by on-chip connection, or it is the level to which the chip back must be connected when specifically stated below. If no potential is given the chip back should be isolated.

Top Material: Al

Backside Material: TiNiAg

Bond Pad Size:  B = .020” X .030”  E = .020” X .030”

Backside Potential: Collector

Mask Ref:

APPROVED BY: DK 			DIE SIZE .100” X .100” 	               DATE:  10/18/12

MFG: ST MICRO			              THICKNESS .010”                                P/N: 2N5154

DG 10.1.2

#### Rev B, 7/19/02

# Text boxes

B

E