Chip back potential is the level which bulk silicon is maintained by on-chip connection, or it is the level to which the chip back must be connected when specifically stated below. If no potential is given the chip back should be isolated.

Top Material: Al

Backside Material: Si

Bond Pad Size:  .004” X .004”

Backside Potential: GND

Mask Ref: M240T

APPROVED BY: DK 			DIE SIZE .062” X .092” 	                   DATE:  3/6/13

MFG: FAIRCHILD			              THICKNESS .014”                                   P/N: 54F240

DG 10.1.2

#### Rev B, 7/19/02

# Text boxes

PAD FUNCTIONS:

- N. OE1

- I0

- N. O4

- I1

- N. O5

- I2

- N. O6

- I3

- N. O7

- GND

- I7

- N. O3

- I6

- N. O2

- I5

- N. O1

- I4

- N. O0

- N.OE2

- VCC

2        1              20                        19

9	      10        11        12

18

17

16

15

14

13

3

4

5

6

7

8

DIE ID