Chip back potential is the level which bulk silicon is maintained by on-chip connection, or it is the level to which the chip back must be connected when specifically stated below. If no potential is given the chip back should be isolated.

Top Material: Al

Backside Material: SiNi

Bond Pad Size: .004” X .004”

Backside Potential: VCC

Mask Ref: 13746

APPROVED BY: DK                        	DIE SIZE  .050” X .054”                         DATE:  4/15/15

MFG: HARRIS	THICKNESS   .012”                               P/N: 54HC132

DG 10.1.2

#### Rev B, 7/1

# Text boxes

PAD FUNCTIONS:

- 1A

- 1B

- 1Y

- 2A

- 2B

- 2Y

- GND

- 3Y

- 3A

- 3B

- 4Y

- 4A

- 4B

- VCC

54 mils

50 mils

12                   11        10               9

2                     3          4                5

13

14

1

8

7

6

MASK

REF