Chip back potential is the level which bulk silicon is maintained by on-chip connection, or it is the level to which the chip back must be connected when specifically stated below. If no potential is given the chip back should be isolated.

Top Material: Al

Backside Material: Si Ni

Bond Pad Size:  .0039” X .0039”

Backside Potential: VCC

Mask Ref:

APPROVED BY: DK 			DIE SIZE .057” X .060” 	               DATE:  2/19/13

MFG: TEXAS INSTRUMENTS                THICKNESS .025”                       	   P/N: 54HC139

DG 10.1.2

#### Rev B, 7/19/02

# Text boxes

PAD FUNCTIONS:

- 1 N.G

- 1A

- 1B

- 1Y0

- 1Y1

- 1Y2

- 1Y3

- GND

- 2Y3

- 2Y2

- 2Y1

- 2Y0

- 2B

- 2A

- 2 N.G

- VCC

DIE ID

2          1       16        15          14

6                   7      8      9                   10

13

12

11

3

4

5

57 mils

60 mils