Chip back potential is the level which bulk silicon is maintained by on-chip connection, or it is the level to which the chip back must be connected when specifically stated below. If no potential is given the chip back should be isolated.

Top Material: Al

Backside Material: Si

Bond Pad Size: .004” X .004”

Backside Potential: GND

Mask Ref: S74G

APPROVED BY: DK                        	DIE SIZE  .049” X .050”                         DATE:  6/5/14

MFG: TEXAS INSTRUMENTS	THICKNESS   .025”                                   P/N: 54S74

DG 10.1.2

#### Rev B, 7/19/02

# Text boxes

PAD FUNCTIONS:

- N. CLR1

- D1

- CLK1

- N. PRE1

- Q1

- N. Q1

- GND

- N. Q2

- Q2

- N. PRE2

- CLK2

- D2

- N. CLR2

- VCC

49 mils

50 mils

1                   14

13

12

11

10

5            6             7              8            9

2

3

4

S74G

MASK

REF