6 Lake Street, Lawrence, MA. 01841

Tel: 1-800-446-1158, (978) 620-2600, Fax: (978) 620-2485

## .064 DIODE GEOMETRY

## BACKSIDE IS CATHODE

| 1. | Chip size………………………… | 64 x 64 Mils nominal |
| --- | --- | --- |
| 2. | Chip thickness………………….. | 10 Mils nominal |
| 3. | Top metal (Anode)……………… | Aluminum 25,000( minimum |
| 4. | Back metal (Cathode)…………… | Gold 4,000( minimum |
| 5. | Bonding pad……………………… | A = 58 x 58 Mils |
| 6. | Tolerances………………………… | All Dimensions ± 2 Mils |
| 7. | Circuit Layout Data……………… | For Zener operation, Cathode must be operated positive with respect to Anode |

# Spec. # T4-4.8-840-012 Rev. 1 (081416)

# Text boxes

CZENR-O64