Chip back potential is the level which bulk silicon is maintained by on-chip connection, or it is the level to which the chip back must be connected when specifically stated below. If no potential is given the chip back should be isolated.

Top Material: Al

Backside Material: CrAgSn

Bond Pad Size: .004” X .004”

Backside Potential: V-

Mask Ref: B

APPROVED BY: DK 			DIE SIZE .034” X .038” 	                   DATE:  3/12/12

MFG: NATIONAL SEMI	                        THICKNESS  .016”	                               P/N: LM134

DG 10.1.2

#### Rev B, 7/19/02